## Slide 1
Hole aware Sparse Read Optimization

## Slide 2: Problem & Motivation
Sparse Files are Everywhere: Virtual Machine disk images (QCOW2, VDI), HPC checkpoint files, database snapshots, and scientific datasets.
The "Hole" Problem:
  Hole: A logical file region with no physical storage allocated. Content is defined as all zeros.
  In a Local File System (e.g., ext4, XFS): Reading a hole is cheap. The OS fills the buffer with zeros locally, with no disk I/O.
In a Networked/Distributed File System (e.g., Lustre, CephFS): The client is unaware of holes. It sends a full READ RPC for the entire range.
Consequences of the Naive Approach:
  Wasteful Network Transfer: The server generates and sends zero-filled pages over the network.
  Unnecessary RPC Overhead: Every hole read incurs a full network round-trip.
  Increased Server Load: Servers waste CPU cycles generating zeros and accessing metadata for non-existent data.
  High Read Latency: Application read time is inflated by this redundant work, especially bad for VM boot and HPC restart times.

## Slide 3: Background: Sparse File Workloads in Detail
Why is this a Pressing Issue? Sparse files are central to key workloads.
High-Performance Computing (HPC) Checkpoint/Restart:
  Pattern: Long-running simulations periodically save state to sparse checkpoint files. Restarting requires reading the entire file.
  Impact: A 100GB checkpoint with 10GB of real data forces 90GB of useless network traffic, drastically slowing job recovery.
Virtual Machine Operations:
  Pattern: Booting a VM reads its sparse disk image (e.g., a 100GB VDI with only ~2GB of OS data). Initial reads hit vast unallocated regions.
  Impact: Directly increases VM startup latency, a critical metric for cloud user experience. Also affects snapshot/clone operations.
Common Trait: These workloads involve reading large logical files where the majority of the requested range may be empty (high sparsity).

## Slide 4: Research Gap & Goal of This Work
State of the Art (NFSv4.2): Introduced READ_PLUS operation. Server can reply with NFS4ERR_HOLE and metadata, telling the client to fill locally.
Limitation: Still requires one RPC per hole read. Good for bandwidth, but not for latency. Uses a weak consistency model.
Goal of our work: Design a transparent optimization for the Lustre parallel file system that:
  Completely avoids RPCs for reading known holes (zero latency).
  Eliminates zero-page transmission for unknown holes (save bandwidth).
  Maintains strong consistency across multiple clients and writers.
  Requires no changes to user applications.

## Slide 5: High-Level Solution: Two Complementary Optimizations
Two-Layer, Orthogonal Approach:
  Layer 1: Client-Side Read Optimization (CSRO)
    Idea: Cache knowledge of hole extents on the client.
    Consistency: protect by extent DLM locks
    Lifecycle: associated with DLM lock lifecycle
    Benefit: For cached holes, serve reads by zeroing memory locally. RPC count → 0.
  Layer 2: Network-layer Sparse Read Optimization (NSRO)
    idea: When a READ RPC must happen, don't send the zero bytes over the wire.
    Benefit: Dramatically reduces network payload. Bandwidth waste → 0.
Key Insight: CSRO is the "fast path" for known holes. NSRO is the "optimized path" for first reads or uncached holes. Together, they cover all cases.

## Slide 6: Design Deep Dive: Client-Side Hole Caching (CSRO)
Core Mechanism: Cache hole extent information on the client under the protection of Lustre's Distributed Lock Manager (DLM) extent locks.
How it Works:
  Hole Discovery: Holes are detected either by the client (during truncate, punch hole) or by the server (during lock grant or a read RPC).
  Caching: Valid hole extents (start, end) are inserted into a per-object Red-Black Tree on the client's Object Storage Client (OSC) layer. Each is "covered" by a DLM lock.
  Fast Path Read: On a read request, the LLITE (top) layer checks the cache. On a hit, it:
    Directly zero-fills the user's page buffer.
    Marks pages as up-to-date.
    Returns immediately, bypassing the entire lower Lustre I/O stack (LOV, OSC, network).
  Consistency: A write or truncate operation acquires a conflicting DLM lock, which triggers a callback to invalidate the overlapping cached hole extent on the client.

## Slide 7: CSRO Lifecycle & Advanced Management
Hole Extent State Machine: Transitions between CACHE (idle) and ACTIVE (serving a read) states. Managed with reference counting.
Intelligent Resource Management: Caching every tiny hole is wasteful.
  Size Threshold: Only cache holes > configurable threshold (e.g., default 64 KiB).
  Extent Coalescing: Merge adjacent or overlapping holes in the RB-tree to reduce overhead.
  Cache Limits & LRU Eviction: Enforce a max number of hole extents per object. Evict least-recently-used on pressure.
Memory Shrinker Integration: Allows the kernel to reclaim hole cache memory under system-wide memory pressure.
Transparency: This is all done within the kernel client. No API changes.

## Slide 8: Design Deep Dive: Network-Layer Sparse Read Opt. (NSRO)
Core Problem: The first read of an uncached hole, or a read from a client without caching, still suffers.
  Core Idea: Modify the RDMA data transfer protocol to skip the zero pages entirely.
  The Sparse PUT (SPUT) Protocol:
Server-side Detection: While processing a READ RPC, the server detects holes in the requested range via the backend filesystem (e.g., SEEK_HOLE).
Decision: If the number/size of holes exceeds a threshold, it triggers NSRO.
Hole Bitmap: The server creates a bitmap describing which pages in the I/O vector are holes (1) and which are data (0).
Modified Transfer: The server initiates an SPUT operation. The header includes the hole bitmap. The RDMA payload contains only the data pages.
Client-side Remapping: The client's LNet layer receives the header, uses the bitmap to remap the destination page vector, leaving "gaps" for holes. It zero-fills those hole pages locally. Data pages are placed directly via RDMA.

## Slide 9: NSRO - Design Choices and Evolutioins LU-16879
Extend LNet Header with extra fxied 32 bytes (256 bits) to store hole bitmap information for sparse reads
  A solution mainly in PtlRPC and LNet layer;
  No need any change in LND driver layer
  Initial version: https://review.whamcloud.com/c/fs/lustre-release/+/55770
  Add extra 32 bytes for other LNET MSG header
First PUT->ACK for hole bitmap info; Second PUT-ACK for the actual IOV data after filtering and re-map
  A solution mainly in PtlRPC and Lnet layer;
  No need any change in LND layer;
  https://review.whamcloud.com/c/fs/lustre-release/+/56788
  Two PUT-ACK round-trips, negative impact on performance
Extend LNet header with variable size for SPUT
  Mainly in PtlRPC and Lnet layer, minor changes in LND layer
  Just one SPUT-ACK round-trip;
  Better performance;
SPUT LND support:
lo LND
sock LND
o2ib LND

## Slide 10: How CSRO and NSRO Work Together
Complementary, Not Redundant.
Scenario A: Reading a cached hole (e.g., sequential read-ahead).
  Path: CSRO Fast Path.
  Network RPCs for full hole: 0.
  Data Transferred for full hole: 0 bytes.
  Good at very large holes.
Scenario B: First read of a large hole.
  Path: Normal I/O path triggers NSRO.
  Network RPCs: 1 (READ request + SPUT reply).
  Data Transferred: Only non-hole data. Holes are filled locally by client LNet.
  Good at high sparsity read (i.e. small holes below CSRO hole threshold but with high sparsity)
Scenario C: Reading a small, uncached hole (below NSRO threshold).
  Path: Fall back to legacy read.
  Network RPCs: 1.
  Data Transferred: Full payload (including zeros). This is the pessimistic case, but management policies (thresholds) minimize its occurrence.

## Slide 11: Comparison with Related Work (NFSv4.2)
Feature NFSv4.2 READ_PLUS This Work (Lustre CSRO+NSRO)
Consistency Weak (close-to-open) Strong (byte-range DLM locks)
Hole Caching No. Every hole read requires a server RPC. Yes. Client caches holes for zero-RPC reads.
RPC Avoidance Impossible by design. Yes, for cached holes.
Network Opt. Returns hole metadata, not data. Good. Returns a bitmap, remaps transfer. Excellent. Can handle multiple holes in one I/O.
Primary Benefit Saves bandwidth. Saves bandwidth AND reduces latency.
Positioning: This work provides a lower-latency, strongly consistent solution, making it ideal for high-performance, multi-writer environments like HPC.
Feature | BeeGFS | NFS | Lustre
Consistency model | Week | Week | Strong
Hole Caching | No | No | Yes
Network Traffic Reduce | No | Medium | High
RPC Avoidance | No | No | Yes

## Slide 12: Patch Status: CNSRO LU-19469
  LU-19469 osc: add tunable for size threshold to cache hole https://review.whamcloud.com/62118
  LU-19469 osc: add hole detect policy tunable https://review.whamcloud.com/62610
  LU-19469 llite: hole-aware read optimization for truncate extend https://review.whamcloud.com/61813
  LU-19469 ldlm: read extent lock req can detect and return holes https://review.whamcloud.com/62453
  LU-19469 ldlm: read extent lock req can detect and return holes https://review.whamcloud.com/62453
  LU-19469 osc: detect holes in read RPCs https://review.whamcloud.com/62586
  LU-19469 osc: add client-side hole caching for hole punch https://review.whamcloud.com/62769
  LU-19469 utils: add lfs commands for hole caching https://review.whamcloud.com/62760
  LU-19469 osc: add lfs hole command to purge caching holes https://review.whamcloud.com/62961
  LU-19469 llite: lfs command to detect/populate hole cache https://review.whamcloud.com/63513
  LU-19469 llite: add hole page stats for read and readahead https://review.whamcloud.com/63515
  LU-19469 osc: prune hole caching for lock BAST with read mode https://review.whamcloud.com/63579
  LU-19469 llite: add hole read optimization for random read https://review.whamcloud.com/63591
  LU-19469 ofd: server-side hole ahead for sequential readahead https://review.whamcloud.com/63708
  LU-19469 osc: pass lu_env to osc_enqueue_upcall_f https://review.whamcloud.com/63769
  LU-19469 osc: add auto LRU shrink for client-side hole caching https://review.whamcloud.com/63798
  LU-19469 llite: add hole pages into client LRU cache list https://review.whamcloud.com/63848
  LU-19469 utils: tool to create or analyze a sparse file https://review.whamcloud.com/62494

## Slide 13: Conclusion
This work presents a holistic solution to the sparse file read problem in distributed file systems, specifically implemented for Lustre.
Key Contributions:
  CSRO: A client-side hole caching mechanism that enables local zero-filling, eliminating RPCs and shortening the I/O path. （LU-19469)
  NSRO: A network-layer optimization using an extended SPUT protocol to skip zero-page transmission, saving bandwidth. (LU-16879)
  A practical design integrating with production infrastructure (DLM, LNet), offering tunable policies and strong consistency.
  Impact: Delivers dramatic performance gains for critical sparse file workloads in HPC and cloud virtualization.
Performance gains (initial simple testing):
  Truncate & read holes: CSRO 50% improvement;
  Full hole read: (two VMs)
    Socklnd TCP/IP protocol
    NSRO disabled: 67.2 MB/s
    NSRO enabled: 1.4 GB/s (almost memory speed - memory copy)